## Slide 1: Pooled Fund Tasks in PaveScan
10/14/20
Roger Roberts GSSI

## Slide 2: Developments June – October 2020
Task 6 - Puck Module Fully Implemented
  Beta-tested at MinnDOT
  Scheduled for Release this week
Task 7 – QA Module Fully Implemented
  Initial beta-testing inhouse scheduled for next week
Task 8 – Core Module 95% implemented
  Completion by end of week
  Initial beta-testing inhouse scheduled for next week

## Slide 3: Puck Module
User-friendly interface for calculating dielectrics of pucks and cores
Generates equation relating compaction to dielectric
Saves calibration equation to file
  can be used by one or more projects
Accessed from desktop short-cut

## Slide 4: Puck Module Quick Walk-Through: Start-up Display
Press Collect
Button

## Slide 5: Select a Project
Typically
one project
per set of pucks

## Slide 6: Project Info
Lots of Project
Information
Can be entered
here.

## Slide 7: File Info
Lots of Puck-specific
Information
can be entered
here

## Slide 8: Collection
Puck dielectric
calculated from sequence of 4 separate measurements

## Slide 9: Playback
Press Playback
Button

## Slide 10: Viewing and Exporting Measurements
See all
measurements
together
Export measurements and all user-entered information

## Slide 11: Viewing Measurements
Auto-loads values
so calibration equation
can be generated without
Manual entries.

## Slide 12: Exported Project

## Slide 13: Quality Assurance Module
Used to:
  Verify antennas are working properly
  Apply dielectric correction to individual channels
3 Methods
  HDPE measurements
  Repeat Line
  Swerve
Integrated into Pavescan
  Collect QA files seamlessly without leaving project

## Slide 14: Data Collection
Select Measurement Type

## Slide 15: Accessing QA Collection
Quality Assurance Measurement Type

## Slide 16: HDPE Measurement Method
S/N 11
S/N 13
HDPE Measurement Method
Press one button at a time to make
10 second measurement

## Slide 17: Other Measurement Methods
S/N 11
S/N 13
Selecting other measurement methods

## Slide 18: Accessing Collected Data
New QA Options
Button in Project
Properties

## Slide 19: View and Apply Correction
Select Correction
Measurement Type
Select how it’s applied

## Slide 20: Multiple Correction Options
Applied in Realtime and Post-Processing

## Slide 21: Core Module
Files specific to core locations
  10 second time file
  6” distance file collected at 40 scans/ft density
Preload core locations
Seamlessly collect files without leaving project
Generate Calibration Equation from collected core files.

## Slide 22: Selecting a Core Measurement
Select Core Measurement Type

## Slide 23: Collecting a Core File
S/N 11
S/N 13
Press one button
to make 10 second
core measurement
Press button
Second time to make 10 second
companion core measurement
Select Time or
Distance method

## Slide 24: Accessing Core Files
New Core Measurement
Button in Project
Info

## Slide 25: Core Measurement Options
Core Calibration
Equation Generation
Import Known Locations