## Slide 1: Density Profiling System Research in North Dakota
Jon Stork, P.E.

## Slide 2: Density Profiling System Research
Need for continuous, non-destructive testing on HMA roadways
  GSSI PaveScan RDM 2.0
TPF-5(443): Continuous Asphalt Mixture Compaction Assessment using Density Profiling System (DPS)
  NDDOT Committed from 2020-2022

## Slide 3: DPS Projects in ND

## Slide 4: Dielectric to Density – ND 32

## Slide 5: Mix Production - Sensitivity
Test 8-1 to 8-3
+0.12% AC
-0.8% AV
No blend changes
+0.8% moisture

## Slide 6: US 83 – Daily Comparison

## Slide 7: NDDOT Research Findings - 2021

## Slide 9: Tips, Tricks & Lessons Learned – PaveScan 2.0
Spare set of RDM batteries
$200 / battery
5-6 hours of collection / set
2. GPS upgrade
Stock unit: Garmin GLO 2
95% <3m accuracy

## Slide 10: Fog Seal
When to collect?
Inconsistent coverage
Process delays

## Slide 11: Joints
Geometry
Double-tacked joints
Notched-wedge joint

## Slide 12: Final Thoughts
Uniformity!
Consistent HMA production/construction
Try it.
Questions?
Jon Stork, NDDOT Material & Research
jstork@nd.gov (701) 328-6903