## Slide 1: 2018 Pavement Workshop May 23-24, 2018
Designing Base & Subbase to Resist Environmental Effects
Steven Henrichs
MnDOT Assistant Pavement Design Engineer
+ 46 Associate Members

## Slide 2: Introduction
Need: MnDOT has pavement design procedures to carry traffic but not for environmental effects.
Objective: A design tool to calculate the depth pavement layers to resist the environment.
Applies only to HMA.
Technical Liaison – myself
Principle Investigator – Matt Oman (& Neil Lund), Braun Intertec

## Slide 3: What Environmental Effects?
Thaw Weakening
Frost Heaving

## Slide 4: Frost Heaving
Water Source
Freezing Air Temperatures
Frost Susceptible Soil
Deepest Advance of Freezing Temperatures
Remains Unfrozen
Frozen Layer
Mixture of Water (in the soil pore structure) and Ice.
Ice Lenses
Ice Lenses
Capillary Rise

## Slide 5: Frost Susceptible soil
Soils that allow capillary rise of water
Sands: Low capillarity and high permeability= low frost susceptibility
Clays: High capillarity but low permeability = low frost susceptibility
Silts: Moderate capillarity and moderate permeability = High Frost susceptibility

## Slide 6: MnDOT Practices
Remove water source with good roadway drainage – surface and subsurface
Make any heave uniform by
Making soils uniform
Matching materials and using transitions
Replace frost-susceptible soil with frost resistant materials

## Slide 7: MnDOT “frost-free material” requirement (Bituminous Pavement)
Pavement
Aggregate Base
Granular Subbase
-*30” for 20-year ESALS ≤ 7 million
- 36” for 20-year ESALS > 7 million
*Approximately ½ of frost depth

## Slide 8: We can do better
Frost depth isn’t the same across the state.

## Slide 9
The frost susceptibility of soils aren't the same.

## Slide 10: Pavement Frost Design Spreadsheet(s)

## Slide 11: Location

## Slide 12: NOAA Freezing index data
State and Station Name | Station Number | Elev. (feet) | Mean Annual Temp. (0 F) | 1.1 Year (10%) | 1.2 Year (20%) | 2 Year (50%) | 2.5 Year (60%) | 3.3 Year (70%) | 5 Year (80%) | 10 Year (90%) | 20 Year (95%) | 25 Year (96%) | 50 Year (98%) | 100 Year (99%) | Lat. (Deg. - Min.)
ADA | 210018 | 906 | 41.1 | 1737 | 2004 | 2487 | 2622 | 2762 | 2919 | 3126 | 3286 | 3331 | 3458 | 3567 | N4718
ALBERT LEA | 210075 | 1220 | 44.8 | 926 | 1162 | 1637 | 1780 | 1934 | 2111 | 2352 | 2546 | 2602 | 2760 | 2899 | N4339
ALEXANDRIA FAA AIRPORT// | 210112 | 1421 | 40.9 | 1774 | 2000 | 2398 | 2507 | 2619 | 2744 | 2906 | 3031 | 3066 | 3163 | 3247 | N4552
ARGYLE 4 E | 210252 | 870 | 37.5 | 2275 | 2578 | 3115 | 3263 | 3415 | 3584 | 3805 | 3975 | 4023 | 4156 | 4271 | N4820
ARTICHOKE LAKE | 210287 | 1075 | 43.2 | 1362 | 1602 | 2047 | 2174 | 2307 | 2456 | 2654 | 2809 | 2853 | 2976 | 3083 | N4522
AUSTIN 3 S | 210355 | 1215 | 44.5 | 1122 | 1320 | 1687 | 1792 | 1901 | 2024 | 2187 | 2315 | 2351 | 2453 | 2541 | N4337
BABBITT 2 SE | 210390 | 1615 | 38.6 | 2010 | 2208 | 2544 | 2634 | 2726 | 2827 | 2956 | 3055 | 3082 | 3159 | 3224 | N4741

## Slide 13: Frost Depth Equation
Frost Depth: General Prediction Model
Pegah Rajaei, Gilbert Y. Baladi

## Slide 14: LTPP Database - SPS-8 Sites
LTPP – Long Term Pavement Performance
SPS-8 – Environmental Effects
<10,000 annual ESALs

## Slide 15: IRI Slope vs Frost Protection Treatment

## Slide 16: Frost Protection Depth vs Silt %

## Slide 17: Soil map

## Slide 18: % Frost Depth Protection

## Slide 19: What’s Next
We’re evaluating it
- Do the calculations appear correct?
Does it need any adjustments?
Can projects be designed with the results?
Can we make it a standard?

## Slide 20
Thank You