## Slide 1: Ingios Geotechnics, Inc.
Presenter:
David J. White, Ph.D., P.E. President and Chief Engineer
david.white@Ingios.com
515-509-7587
Contact Info:
www.ingios.com
1-877-325-6278

## Slide 2: Ingios Geotechnics, Inc: Solutions
APLT*
Pavement System Mechanistic Verification and Optimization
Verify in situ stress-dependent resilient modulus for AASHTOWare™ Pavement ME
Predict permanent deformation performance over life of pavement loading
Assess multi-layer modulus
Test crack resistance of HMA
VIC*
Validated Intelligent Compaction (VIC) Control
Real-time monitoring results
Automated reporting
Advanced software tools
Efficient data management, sharing, and alert notifications
IMAS*
Accelerated Pavement Testing
1,000,000 loading cycles
Pre-design verification of alternative systems
Verify in situ stress-dependent resilient modulus for AASHTOWare™ Pavement ME

## Slide 3
Options for Engineering Outputs:
Mr, Es, k-value, CBR, gd*, w%*, Material type
Options for GNSS:
SBAS (WAAS), OmniSTAR, D-GPS, RTK-GPS, dual antenna, IMUs
Validated Intelligent Compaction (VIC)
Outputs:
Real-Time Monitoring
Engineering Reports
Email Alert Messages
Control charts
Calibration Verification
WebCam and Pictures
QC/QA Records
Asset Mapping
QC/QA Test Locations
Compaction Cost Analyzer
Customizable solutions for each machine, each site, and each customer.
Layer 1
Layer 2
Layer 3
Sensor
Sensor
Position Sensors
Vibrating Drum
Vibrations transmitted into ground
Computer screen showing spatial color-coded data overlain on georeferenced aerial image

## Slide 4
Integrate sensor package into machine (options for stress-dependent modulus, 40+ different material outputs, and material/moisture vision system)
VIC is field calibrated using APLT for site conditions
Display real-time results to operator and via real-time CID dashboard system
Auto-generate compaction reports and alert messages to team, including function for P.E. review
Use advanced desktop software to analysis multi-layer properties and identify areas for QA/QC testing
Identify areas for improvement (not compaction)
Improve compaction efficiency and reduce risk of poor-quality
Ingios Technology Validated Intelligent Compaction (VIC)
How it works…

## Slide 5: Geo-materials are complex and highly variable

## Slide 6
Material Name | Material Type ID | Color
Other | 0 | 
Fly Ash | 1 | 
Bottom Ash | 2 | 
Gypsum | 3 | 
Subgrade_1 | 4 | 
Subgrade_2 | 5 | 
Subgrade_3 | 6 | 
Aggregate Base_1 | 7 | 
Aggregate Base_2 | 8 | 
Aggregate Base_3 | 9 | 
Glacial Till | 10 | 
Grey Clay | 11 | 
Red Clay | 12 | 
Brown Clay | 13 | 
Dark Clay | 14 | 
Light Clay | 15 | 
Silt | 16 | 
Sand | 17 | 
Silty Clay | 18 | 
Silty Sand | 19 | 
Gravel | 20 | 
Subbase | 21 | 
RAP | 22 | 
RPCC | 23 | 
Cement Stabilized Subgrade | 24 | 
Cement Stabilized Base | 25 | 
Lime Treated Subgrade | 26 | 
Stabilized Subgrade | 27 | 
Treated Subgrade | 28 | 
Stabilized Aggregate Base | 29 | 
Limestone | 30 | 
Modified Subbase | 31 | 
Select backfill | 32 | 
PGE | 33 | 
CA6 | 34 | 
Class 5 Aggregate Base | 35 | 
OGB | 36 | 
0.75-inch minus | 37 | 
1-inch minus | 38 | 
1.5-inch minus | 39 | 
Ingios Technology Validated Intelligent Compaction (VIC)
We have initiated a database of common material types to assist contractors with initial pre-calibration process.

## Slide 7: Ingios is redefining quality compaction
CQI ≥ [95]
[80%] of [XMV] MVs ≥ [XMV_TV]
COV of MVs ≤ [20%]
VIC QUALITY ANALYSIS
i-Score Blob ≤ [200 ft2]
[80%] of [w%] ≥ w%_TV
112.5
98.5
0.321
138
69.8
CQI = Compaction Quality Index. CQI is a measure of the compaction quality in terms of the percentage of VIC measurement values (MVs) (e.g., XMV) greater than the target value (TV) and the variability of the MVs in terms of coefficient of variation (COV). CQI is higher for higher MVs and lower variability.
w% = Moisture Content. w% is determined from the VIC vision sensor kit and based on statistical calibration from laboratory samples.
i-Score is a statistical measurement of a VIC measurement value (MV) (e.g., k-value) compared to the mean score within a map. An i-Score of 0 means the score is the same as the mean. An i-Score Blob is a contiguous (i.e., connected) group of MVs with an i-Score less than the target score value. i-Score Blobs show potential “bad” areas.
COV of MVs = Coefficient of Variation of the Measurement Values. COV is calculated as the standard deviation of the measurements divided by the average value.
_% of MVs = Percentage of VIC measurement values (MVs) (e.g., XMV) greater than the target value (TV) for a map area.

## Slide 8: Ingios Customizable Dashboard System for Compaction Quality Assessment (Compaction Intelligence Dashboard)

## Slide 9: Ingios Dashboard – Mobile

## Slide 11: Ingios Modulus VIC System
Sensors

## Slide 12
Automated Plate Load Testing Report:
I-294 NB and SB Lanes, MP. 17.5 to 40.0,
95th Street to Balmoral Ave
“The Tollway’s objective is to design and reconstruct this section of expressway in the most cost efficient manner for the life of the pavement.”
“ With the APLT technology, we now have actual measurements of how well the subgrade will support the pavement, so we can avoid overdesign.”
Steve Gillen, PE — IL Tollway Materials Manage

## Slide 13: Ingios: Accelerated Testing System

## Slide 14: Tenets of measurement …
Tenets of Pavement Foundation Measurement |  | 
PROJECT NAME: |  | 2017 MnROAD Unbound Layer Evaluation Using Intelligent Compaction
PROJECT ID: |  | MnROAD_IC
LOCATION: |  | MnROAD, Albertville, Wright County, MN
Performance of pavements is directly coupled to the support provided by the pavement foundation layers and embankment.
Pavement foundation layer stiffness (resistance to deformation in response to an applied stress), permanent deformation (deformation not recovered from removal of applied stresses), and uniformity of support (localized variations) are critical factors affecting pavement performance, and therefore need to be measured to verify construction quality.
By measuring the critical engineering properties and understanding how they affect performance, pavement design methodologies can be improved. With improvements to design, pavement system performance can be optimized and risks of performance problems can be reduced.

## Slide 15
PROJECT NAME: |  | 2017 MnROAD Unbound Layer Evaluation Using Intelligent Compaction
PROJECT ID: |  | MnROAD_IC
LOCATION: |  | MnROAD, Albertville, Wright County, MN
VIC Mapping Test Sections
Low Volume Road, MnRoad
SUMMARY
06/26/2017 to 09/01/2017
On Site Personnel
David J. White (Ingios)
Pavana Vennapusa (Ingios)
James Colby Van Nimwegen (Ingios)

## Slide 16
Sections reworked
to include geosynthetic/geogrid at subbase/subgrade interface
SUMMARY OF DIFFERENT CROSS-SECTIONS W/ VIC MAPPING |  | 
PROJECT NAME: |  | 2017 MnROAD Unbound Layer Evaluation Using Intelligent Compaction
PROJECT ID: |  | MnROAD_IC
LOCATION: |  | MnROAD, Albertville, Wright County, MN
6 in. Class 5Q Aggregate Base
Sand Subgrade
Cells 124-424
Cells 138-238
Existing Material
Mixture of existing subgrade and base material
Clay Loam Subgrade
Cells 139-239
Clay Loam Subgrade
Cells 139-239
6 in. Class 5Q Aggregate Base
4 in. Common Borrow
Sand Subgrade
Cells 185-186
12 in. Coarse (Cell 185) or Fine (Cell 186) Recycled Concrete Aggregate Base
3.5 in. Common Borrow
Clay Subgrade
Cells 188-189
12 in. Recycled Aggregate Base (Cell 189) or Crushed Limestone Base (Cell 188), Class 6
3.5 in. Common Borrow
Cells 133-235
Existing Base Material
Cells 133-235
Existing Base Material
Cold Central Plant Rec. AC
Clay Subgrade
Cells 127-227
18 in. Large Aggregate Subbase
Clay Subgrade
Cells 128-228
9 in. Large Aggregate Subbase
Clay Subgrade
Cells 127-227
18 in. Large Aggregate Subbase
6 in. Class 6 Aggregate Base
Clay Subgrade
Cells 128-228
9 in. Large Aggregate Subbase
6 in. Class 6 Aggregate Base
Cell 227 – subbase placed in 2 lifts (9 in. each), Cell 127 – subbase placed in 1 lift
Cell 227 – subbase placed in 2 lifts (9 in. each), Cell 127 – subbase placed in 1 lift

## Slide 17
STATE | PAVEMENT | DESIGN DESCRIPTION | SUBGRADE INPUTS | BASE/SUB-BASE INPUTS
CA | Flexible | HMA and base/subbase layer thickness based on R-value of the subgrade and Traffic Index | R-Value1 | R-Value1
 | Rigid | PCC and base/subbase layer thickness based on R-value of the subgrade and Traffic Index | R-Value1 | Mr 2
IL | Flexible | Modified AASHTO Design procedure. Thickness design based on traffic factor and estimated structural number. | IBR value | Structural layer coefficients (a2, a3)
 | Rigid | Modified AASHTO Design procedure. Thickness design based on traffic factor and IBR or k-value. | IBR value or k-value3 | N/A [only minimum thickness]
MI | Flexible | Pavement ME Design [Similar to AASHTOWareTM] – Level 2 or 3 (Typical values) | Mr2 | Mr 2
 | Rigid | Pavement ME Design [Similar to AASHTOWareTM] – Level 2 or 3 (Typical values) | Mr 2 | Mr 2
MO | Flexible | AASHTO Pavement ME Design | Mr 6 | Mr 6
 | Rigid | AASHTO Pavement ME Design | Mr 6 | Mr 6
MN | Flexible | MnPAVE-Flexible with basic, intermediate, and advanced level. Advanced level requires moduli of all layers, while basic and intermediate levels require typical values or DCP test results, R-value results. | R-value4 (basic/int) or Mr (advanced) | DCP index4 (basic/int) or Mr (advanced)
 | Rigid5 | MnPAVE-rigid uses MEPDG level 3 based design procedure. | Mr | Mr
WI | Flexible | AASHTO 1972 design procedure. Thickness design based on design ESALs, soil support value, and estimated structural number. | Soil support value (correlated to CBR) | Structural layer coefficients (a2, a3)
 | Rigid | AASHTO 1972 design procedure. Thickness design based on design ESALs, working stress, and modulus of subgrade reaction (k) | k-value | NA
Summary of pavement foundation layer inputs for NRRA participating states.
1California R-value is a measure of resistance to deformation of the soils under saturated conditions and traffic loading as determined by the stabilometer test (CT301). Typical range between 5 (very soft) to 80 (treated base material). Typical values provided based on soil classification/ region.
2Typical resilient moduli vales are provided in the design guide based on the material type.
3Illinois bearing ratio (IBR) is a slight modification of CBR test run after 4-days of soaking. Typical values are provided based on soil classification (ranges between 2 and 20). Modulus of subgrade reaction (k) value vs. IBR is provided in the design nomographs.
4Minnesota R-value determined from modulus value (R = [0.41+0.873*(subgrade modulus/1000)]^1.28)
5MnPAVE-Rigid design procedure for PCC bonded overlay over HMA uses the ACPA procedure to determine composite k-value based on subgrade k-value and aggregate layer resilient modulus. http://apps.acpa.org/applibrary/KValue/
6personal communication, 03/02/2017, John P. Donahue, P.E., Construction and Materials Liaison Engineer, MoDOT
CalTrans Highway Design Manual - http://www.dot.ca.gov/hq/oppd/hdm/pdf/english/HDM_Complete_07Mar2014.pdf
ILDOT Pavement Design Manual - http://www.idot.illinois.gov/Assets/uploads/files/Doing-Business/Manuals-Split/Design-And-Environment/BDE-Manual/Chapter%2054%20Pavement%20Design.pdf
MDOT User Guide for ME Pavement Design: https://www.michigan.gov/documents/mdot/MDOT_Mechanistic_Empirical_Pavement_Design_User_Guide_483676_7.pdf
MnDOT Pavement Design Manual: www.dot.state.mn.us/materials/pvmtdesign/manual.html
WIDOT Facilities Development Manual: http://wisconsindot.gov/rdwy/fdm/fd-14-10.pdf

## Slide 18
Ingios VIC Record – VIC_Mr-SG @ 10 psi Plate Contact Stress |  | 
PROJECT NAME: |  | 2017 MnROAD Unbound Layer Evaluation Using Intelligent Compaction
PROJECT ID: |  | MnROAD_IC
LOCATION: |  | MnROAD, Albertville, Wright County, MN
DATE: |  | 08/17/2017
OPERATOR: |  | PV (Ingios)
< 8 ksi
10 ksi
15 ksi
20 ksi
Mr-SG
12 ksi
30 ksi
40 ksi
>40 ksi
0
125
250
375
500
Feet
Clay Subgrade
Cells 127-227
Cross-Section
18 in. Large Aggregate Subbase
VIC Calibration
Test Points
8
7
6
5
VIC Calibration
Test Points
Cell 227 – subbase placed in 2 lifts (9 in. each), Cell 127 – subbase placed in 1 lift
MAP ID: |  | Cells 127/227_Subbase | 
Surface Material: |  | Subbase | 
Mapping Time: |  | 5 min | 4 min
No. of Measurements: |  | 332 | 412
Meas. Property: |  | Mr-SG @ 10 psi plate contact stress | 
Mean: |  | 12.9 ksi | 11.7 ksi
Standard Deviation: |  | 3.1 ksi | 2.6 ksi
Coeff. Of Variation: |  | 24% | 22%
Machine: |  | CS56
Drum Configuration: |  | Smooth
Vibration Settings: |  | f = 30 Hz, low amp
Speed: |  | 3 mph (nominal)

## Slide 19
< 8 ksi
10 ksi
15 ksi
20 ksi
Mr-Base
12 ksi
30 ksi
40 ksi
>40 ksi
Ingios VIC Record – VIC_Mr-Base @ 10 psi Plate Contact Stress |  | 
PROJECT NAME: |  | 2017 MnROAD Unbound Layer Evaluation Using Intelligent Compaction
PROJECT ID: |  | MnROAD_IC
LOCATION: |  | MnROAD, Albertville, Wright County, MN
DATE: |  | 08/17/2017
OPERATOR: |  | PV (Ingios)
0
125
250
375
500
Feet
Clay Subgrade
Cells 127-227
Cross-Section
18 in. Large Aggregate Subbase
VIC Calibration
Test Points
8
7
6
5
VIC Calibration
Test Points
Cell 227 – subbase placed in 2 lifts (9 in. each), Cell 127 – subbase placed in 1 lift
MAP ID: |  | Cells 127/227_Subbase | 
Surface Material: |  | Subbase | 
Mapping Time: |  | 5 min | 4 min
No. of Measurements: |  | 332 | 412
Meas. Property: |  | Mr-Base @ 10 psi plate contact stress | 
Mean: |  | 21.3 ksi | 15.4 ksi
Standard Deviation: |  | 4.8 ksi | 4.1 ksi
Coeff. Of Variation: |  | 23% | 26%
Machine: |  | CS56
Drum Configuration: |  | Smooth
Vibration Settings: |  | f = 30 Hz, low amp
Speed: |  | 3 mph (nominal)

## Slide 20
Ingios VICM Calibration Record |  | 
PROJECT NAME: |  | 2017 MnROAD Unbound Layer Evaluation Using Intelligent Compaction
PROJECT ID: |  | MnROAD_IC
LOCATION: |  | MnROAD, Albertville, Wright County, MN
Mr-Comp @ 10 psi cyclic stress
using 12 in. diameter loading plate
k1 and k2 values for 30 in. diameter static plate load test
NOTE: Ingios VICM calibration record provided below are results from recent off-site calibration (June 21-22, 2017) performed on the CS56 smooth drum vibratory roller used at MnROAD. The calibration plots summarize the calibration validity range for the three measurement parameters presented, coefficient of determination (R2) value, and the standard error (RE) values of the measured versus predicted values. Site and material specific calibration is planned for August 14-18 cell construction.
Composite Resilient Modulus at 10 psi cyclic stress
Modulus of Subgrade Reaction at 10 psi (initial load)
Modulus of Subgrade Reaction at 10 psi (reload)

## Slide 21
Box and Jitter plots of Mr-Comp @ 30 psi plate contact stress |  | 
PROJECT NAME: |  | 2017 MnROAD Unbound Layer Evaluation Using Intelligent Compaction
PROJECT ID: |  | MnROAD_IC
LOCATION: |  | MnROAD, Albertville, Wright County, MN
[124-424]
Box Plots – Mr-Comp_30 psi
[138-238]
[133-235 CCRP]
[133-235 Base]
[139-239]
[188-189]
[185-186]
[127-227]
[228:BX]
[128:TX]
[228:F+BX]
[128:F+TX]

## Slide 22: Thank you.
Contact Info:
www.ingios.com
1-877-325-6278
Office Locations:
Northfield, MN (David J. White, Ph.D., P.E.)
Little Elm, TX (Pavana Vennapusa, Ph.D., P.E.)
Ames, IA (E. Thomas Cackler, P.E.)
Boston, MA (Brendan FitzPatrick, P.E.)