## Slide 1: National Road Research Alliance Flexible Team Update
Barry Paye, PE – Wisconsin DOT
Chief Materials & Pavement Engineer
Barry.paye@dot.wi.gov

## Slide 2: NRRA - Flexible Team Update Team Members
Agency Members
Paul Denkler, Missouri Department of Transportation Shongtao Dai, Minnesota Department of Transportation James Foldesi, St. Louis County Minnesota Kee Foo, Caltrans – California Department of Transportation John Garrity, Minnesota Department of Transportation Steve Hefel, Wisconsin Department of Transportation Kevin Kennedy, Michigan Department of Transportation Dan Kopacz, Wisconsin Department of Transportation Dan Oesch, Missouri Department of Transportation Greg Olson, North Dakota Department of Transportation Barry Paye (Chair), Wisconsin Department of Transportation Raghubar Shrestha, Caltrans – California Dept of Transporation Jim Trepanier, Illinois Department of Transportation Charles Wienrank, Illinois Department of Transportation Tyler Wollmuth, North Dakota Department of Transportation

## Slide 3: NRRA - Flexible Team Update Team Members
Associate Members
Jay Bianchini--Collaborative Aggregates Justin Black--Cargill Brandon Brever --Minnesota Asphalt Pavement Association (MAPA) Tom Brovold--Testquip Gina Buccelato--3M Transportation Safety Division Mike Byrnes--Mathy Construction Co. Andy Cascione--Flint Hills Resources Jo Sias Daniel--University of New Hampshire Stacy Glidden--Payne & Dolan Kris Hansen-- 3M Transportation Safety Division David J. Jones--University of California Pavement Research Center Nathan Just--Caterpillar Paving Products Lev Khazanovich--University of Pittsburgh Brett Lambden--Husky Energy Todd Mansell--Caterpillar Paving Products

## Slide 4: NRRA - Flexible Team Update Team Members
Associate Members - Continued
Mihai Marasteanu--University of Minnesota – Twin Cities Ken Maser--Infrasense Kiran Mohanraj--Transtec Group Dave Rettner--American Engineering Testing Mohammad Reza Sabouri--Braun Intertec Guy Sisler--Husky Energy Dan Staebell--Asphalt Pavement Alliance (APA) Brandon Strand--Asphalt Pavement Alliance (APA) Kim Tolzmann--Hardrives Randy West--National Center for Asphalt Technology (NCAT) Jason Wielinski, ARRA Chris Winiecki--Payne & Dolan Zhanping You--Michigan Tech Transportation Institute

## Slide 5: NRRA - Flexible Team Update Team Members
Friends & Supporting Staff
Ryan Baasen, Minnesota Department of Transporation Brian Bennes,North Dakota Department of Transportation Tim Clyne, Minnesota Department of Transportation Dave Van Deusen, Minnesota Department of Transportation Curt Dunn, North Dakota Department of Transportation Mohamed Elkashef--University of California Pavement
Research Center Jerry Geib, Minnesota Department of Transportation Kevin Kliethermes, FHWA Joe Korzilius, SRF Consulting Renae Kuehl, SRF Consulting Korby Seward, North Dakota Department of Transportation Ben Worel, Minnesota Department of Transportation

## Slide 6: NRRA - Flex Team Update Website

## Slide 7: NRRA - Flex Team Update Website

## Slide 8
SRF Consulting
NRRA Team | Topic
Flexible | Tack Coats
 | Longitudinal Joint Construction Performance
Rigid | Design and Performance of Concrete Unbonded Overlays
 | Repair of Joint Associated Distress Pavements
Geotechnical | Larger Subbase Materials
 | Subgrade Design for New and Reconstructed Roadways
Pavement Maintenance | Surface Characteristics of Diamond Ground PCC Surfaces
 | Pavement Preservation Approaches for Lightly Surface Roadways
2017 Short Term Research
Notes: Team Leads Discuss each topic

## Slide 9: Short Term Research – Longitudinal Joints
Notes: From the Preventive Maintenance , home page, click on links to all the project web pages.

## Slide 10: Short Term Research – Tack Coats
Notes: From the Preventive Maintenance , home page, click on links to all the project web pages.

## Slide 11
SRF Consulting
NRRA Team | Topic
Flexible | NRRA - Mix Rejuvenator Synthesis (Phase-1) – 1:00 on Thursday
Pavement Maintenance | NRRA Spray on Rejuvenator Synthesis
 | Service Life Enhancement of Substrates Overlaid with Thin Overlays (UTWBC, Chip Seals & Microsurfacing)
 | Concrete Pavement Restoration (CPR) for Bonded Concrete Overlays of Asphalt (BCOA)
2019 Short Term Research Technology Transfer
Notes: Team Leads Discuss each topic

## Slide 12: Long Term Research Flexible Team
Team | Projects | Contractor
2017 Flexible | HMA Overlay of PC and Methods of Enhancing Compaction | University of New Hampshire
 | Cold Central Plant Recycling | American Engineering and Testing
2019 Flexible | Mix Rejuvenator Test Sections (Phase-II) | TBD
Notes: Team Leads Discuss each topic

## Slide 13: Long Term Research Flexible Team
Team | Projects | Contractor
2017 Flexible | HMA Overlay of PC and Methods of Enhancing Compaction | Update – 12:45 Today
 | Cold Central Plant Recycling | Update – 12:45 Today
2019 Flexible | Mix Rejuvenator Test Sections (Phase-II) | TBD
Notes: Team Leads Discuss each topic

## Slide 14
2017 - HMA Overlay and Rehab of Concrete and Enhancing Compaction

## Slide 15
HMA Overlay and Rehab of Concrete and Methods of Enhancing Compaction
  12 Test Sections + 1 Control
  7 unique Mixes
  3/4” - 1.5” - 4” Overlays
  1 Undersealing PCC
DESCRIPTION | CELL | DEPTH (inch) | MIX DESCRIPTION (NMAS, mm) | BINDER | DESIGN VOIDS
Control Section | 983 | - | - | - | -
HMA over PCC (1 lift) | 984 | 1.50 | Superpave (9.5) | 58H-28 | 4.0
 | 985 | 1.50 | Superpave (12.5) | 58H-28 | 4.0
 | 986 | 1.75 | Superpave (12.5) | 58H-28 | 4.0
HMA over PCC (2 lifts) | 987 | 1.50 | Superpave (9.5) | 58H-28 | 4.0
 |  | 2.50 | Superpave (19.0) | 58H-28 | 4.0
HMA over PCC (2 lift) | 988 | 1.75 | Superpave (12.5) | 58H-28 | 4.0
 |  | 2.25 | Superpave (19.0) | 58H-28 | 4.0
 | 989 | 1.75 | Superpave 95/5 (12.5) | 58H-28 | 5.0
 |  | 2.25 | Superpave (19.0) | 58H-28 | 4.0
 | 990 | 1.75 | Regressed voids design (12.5) | 58H-28 | 3.0
 |  | 2.25 | Superpave (19.0) | 58H-28 | 4.0
 | 991 | 1.75 | Superpave (9.5) | 58H-28 | 4.0
 |  | 2.25 | Superpave (19.0) | 58H-28 | 4.0
HMA over PCC w/interlayer | 992 | 1.50 | Superpave (9.5) | 58H-28 | 4.0
 |  | 1.00 | Crack inhibiting interlayer (4.75) | 58E-34 | 2.0-3.0
HMA over PCC w/PASSRC | 993 | 1.50 | Superpave (9.5) | 58H-28 | 4.0
 |  | 1.00 | Permeable interlayer mix | 64S-22 | -
HMA over PCC (1 lift) | 994 | 1.50 | Superpave (9.5) | 58H-28 | 4.0
 | 995 | 0.75 | Ultra-Thin Bonded Wearing Course with PCC/Soil Stabilization | 58V-34 | -

## Slide 16
Cold Central Plant Recycling
  4 Test Sections
    Foam vs Emulsion
    2X Chip vs 1.5” HMA Overlay
  How can states be green in recycling but not impact long term performance?

## Slide 17: NRRA – Flex Team Update Rejuvenator Project
Save for Rejuvenator project map and companies
Format Suggested (28 font)
  Details (24 font)
    Details (24 font)
TH 6 from Emily to Outing

## Slide 18: NRRA – Flex Team Update Rejuvenators
Anticipated Participants:
Cargill
Collaborative Aggregates
Asphalt and Wax Innovations
Superior Bowen
Mathy
Kraton
Georgia Pacific
Poet
Ingevity
U.S. Soybean Board
Testing Program:
Laboratory Testing
Field Performance Monitoring

## Slide 19: NRRA – Flex Team Update
Any Questions?
Barry Paye, PE
Wisconsin DOT
Barry.paye@dot.wi.gov
608-246-7945

## Slide 20
Questions or Comments?