## Slide 1: Rigid Team Update
Brett Trautman, P.E.
Physical Laboratory Director
Construction & Materials Div.
Missouri DOT
2019 Pavement Workshop May 21-23, 2019
+ 46 Associate Members
Office No.: 573-751-1036
Email: Brett.Trautman@modot.mo.gov

## Slide 2: Outline
Review Short Term Research -2017
Review Long Term Research – 2017
Phase II Research - 2019
Compacted Concrete Pavement - 2018

## Slide 3: Review Short Term Research - 2017
Design and Performance of Concrete Unbonded Overlays
Repair of Joint Associated Distress Pavements

## Slide 4: Design and Performance of Concrete Unbonded Overlays
Synthesis of member states
Survey
Questions on design features and field performance (good & bad)
Contractor is SRF Consulting
First draft completed

## Slide 5: Repair of Joint Associated Distress Pavements
Develop technical brief based on current knowledge & expertise
Develop one hour webinar
Contractor is SRF Consulting
Dr. Peter Taylor with Iowa State University assisting

## Slide 6: Review Long Term Research - 2017
FRC Research
Early Opening Strength
Reduced Cementitious Material

## Slide 7: FRC Research
  Determine contribution of fibers in reducing panel fatigue cracking
  Determine contribution of fibers in mitigating joint faulting
  Determine optimal panel size for thin unbonded concrete overlays
  Determine minimum thickness of FRC for low-volume streets
Objectives
Contractor
University of Minnesota – Duluth (Dr. Manik Barman)

## Slide 8: FRC Research
Mainline Cell #6 (506, 606, 706, & 806)
Evaluating the impact fiber dosage has on fatigue cracking & joint faulting
Cell No. | 506 | 606 | 706 | 806
Length | 144 ft. | 138 ft. | 138 ft. | 138 ft.

## Slide 9: FRC Research
  Full depth pavement on grade
  All cells: 6’ x 6’ panels
  Fiber content:
  Cell 506: No fibers (control)
  Cell 606: 20% RSR
  Cell 706: 30% RSR
  Cell 806: 0.75% fibers by volume
Pavement Details (Cell #6)

## Slide 10: FRC Research
Mainline Cell #5 (705 & 805)
Evaluating the impact fibers have on fatigue cracking, joint faulting, & panel size
Cell No. | 705 | 805
Length | 144 ft. | 124 ft.

## Slide 11: FRC Research
  Unbonded Overlay
  - Non-woven geotextile fabric interlayer
  Cell 705
  - 14’W x 12’L & 12’x12’ panels
  Cell 805
  - 6’ Wx12’L & 8’Wx12’L panels
  Fiber content: 20% RSR
Pavement Details (Cell #5)

## Slide 12: FRC Research
Low Volume Road Cell #39 (139 & 239)
Evaluate using fiber-reinforced concrete pavement for city streets
Cell No. | 139 | 239
Length | 270 ft. | 273 ft.

## Slide 13: FRC Research
All cells: 6’ x 6’ panels
Full depth concrete on grade
Fiber content: 30% RSR
Pavement Details (Cell #39)

## Slide 14: Early Opening to Traffic
  Evaluate visible and non-visible immediate damage caused by early age loading
  Quantify the effect of early loading damage on long-term performance
  Determine minimum strength at opening or other measurable variables associated with this parameter
Objectives
Contractor
University of Pittsburg (Dr. Lev Khazanovich)

## Slide 15: Early Opening to Traffic
Low Volume Road Cell #24 (124, 224, 324, 424, 524 & 624)
Early sequential traffic loadings
Cell No. | 124 | 224 | 324 | 424 | 524 | 624
Length | 120 ft. | 120 ft. | 120 ft. | 115 ft. | 60 ft. | 20 ft.

## Slide 16: Early Opening to Traffic
  Standard panel size 12’W x 15’L
  Full depth concrete on grade
  Standard concrete mix
  Doweled joints
Pavement Details (Cell No. 24)

## Slide 17: Reduced Cementitious Content
Objectives
  Investigate the early-age characteristics of concrete paving mixes containing low cementitious content
  Assess the potential for durability issues
  Identify effect of reduced cementitious content on long term serviceability and economics
  Develop recommended specifications for mixing and placement practices
Contractor
Iowa State University (Dr. Peter Taylor)

## Slide 18: Reduced Cementitious Content
Low Volume Road Cell #38 (138 & 238)
Cells will be exposed to deicing agents
Cell No. | 138 | 238
Length | 258 ft. | 260 ft.

## Slide 19: Reduced Cementitious Content
Pavement Details (Cell No. 38)
Standard panel size 12’W x 15’L
Full depth concrete on grade
Doweled Joints
Cell 138
- Cementitious content = 500 lb./cy
Cell 238
Cementitious content = 470 lb./cy

## Slide 20: Phase II Research - 2019
Construction Report for Jointless Roundabout
Iowa State University ($50,000)
Incorporate Faulting Model To BCOA-ME
University of Pittsburg ($25,000)
Determination of Causes for Cracking Over Dowel and Tie Bars
Posting RFP ($100,000)

## Slide 21: Construction Report for Jointless Roundabout
Roundabout constructed in Minnesota in 2018
Document project activities
Mix design, placement, test results & field issues
Document Initial Distresses
12 cracks noted to date
Field Monitoring
Three years

## Slide 22: Incorporate Faulting Model To BCOA-ME
Adding faulting model to the existing BCOA program in Pavement-ME
PennDOT currently funding research to add faulting model to program
Only for Pennsylvania
NRRA funding to have program incorporate national inputs

## Slide 23: Determination of Causes for Cracking Over Dowel and Tie Bars
Two SPS-2 projects noted this issue
Other states have observed
Research being divided into two phases
Phase 1: Conduct literature review, examine pavements, obtain samples from pavements and design laboratory experiments

## Slide 24: Compacted Concrete Pavement

## Slide 25: Big Thanks!!
Emery Sapp & Sons
Andale
Euclid
National Road Research Alliance (NRRA)
Minnesota DOT
Missouri University Science & Technology
Southeast District - MoDOT

## Slide 26: What is Compacted Concrete Pavement (CCP)?
Similar to RCC
Zero slump
Consolidate by compacting
No air entrainment
Significant Differences
Utilize a high density paver
Utilize special admixture
Apply special finishing aid
Broom Texture

## Slide 27: NRRA Involvement
Rigid Team selected CCP
Cost more than anticipated
SE District added CCP to a project
Contract awarded
MoDOT asked if NRRA funds could be used for research
First NRRA satellite project

## Slide 28
Where

## Slide 29: Project Location
Outer Road – East side of I-55
Scott County
Approx. 2 miles
Test Strip on Oct. 24
Full Production started on Oct. 25
- SBL placed first

## Slide 30: Pavement Structure
Plans
Proposed
8” CCP
6” CCP
6” Type V Base
4” Type V Base
12” Soil Stabilization

## Slide 31: Mix Design Criteria
Cementitious Content: 550 lbs./C.Y.
Fly Ash Amount: 18%
w/cm Ratio: 0.38
Amount of Fine Aggregate: 35% (by agg. vol.)
Max. Aggregate Size: 1-inch
Special Admixture: ACEit
Fibers: 5 lbs./C.Y. of 2-inch macro fibers

## Slide 32: Concrete Plant

## Slide 33: Concrete Plant

## Slide 34: Concrete Plant

## Slide 35: Adding ACEit Admixture

## Slide 36: Macro Fibers
5 lbs./cu. yds.
2 in. length

## Slide 37: Adding Fibers

## Slide 38: High Density Paver

## Slide 39: Stringless Paving

## Slide 40: CCP Placement

## Slide 41: Density Testing
Typically 98% behind the paver

## Slide 42: Finishing CCP

## Slide 43: Finishing CCP

## Slide 44: Texturing CCP

## Slide 45: Curing

## Slide 46: Sawing

## Slide 47: Test Sections
Constructed three test sections (SBL’s)
Test Section No. 1 (495 ft.)
15 ft. joint spacing
No fibers
Test Section No. 2 (504 ft.)
12 ft. joint spacing
No fibers
Test Section No. 3 (255 ft.)
15 ft. joint spacing
5 lbs./C.Y. macro fibers utilized

## Slide 48: Sensor Layout
Thermocouple Tree
Joint Opening
Block Out
Vibrating Wire Strain Gauges
Dynamic Strain Gauges
Dynamic Strain Gauges

## Slide 49: Installing Sensors

## Slide 50: Test Section No. 1
Looking North

## Slide 51: Test Section No. 2
Looking North
Looking South

## Slide 52: Test Section No. 3
Looking North
Looking South

## Slide 53: Test Section No. 3

## Slide 54: CCP with Fibers

## Slide 55: Samples Molded
Missouri University of Science & Technology
Missouri DOT

## Slide 56: Extracting Samples

## Slide 57: Extracting Samples

## Slide 58: Falling Weight Deflectometer

## Slide 59: Lessons Learned
Moisture content critical
Load truck in two dumps
Utilize surge hopper (prevent dumping wings)
Tunnel extensions fully charge
Monitor mixture consistence (each load)
Adjust amplitude & frequency of tamper screed
Wet Load Decrease Energy
Dry Load Increase Energy

## Slide 60
Questions or Comments?