## Slide 1
Chapter 6 Signing Plan Design & Plan Sets
Sign Plan Design for
At-Grade Intersections
June 2017

## Slide 2: Signing Plan Assembly Steps
Download latest plan set assembly steps from OTST website
Sample plans organized to follow an established format
When proceeding through steps, refer to sample plans

## Slide 3: Signing Plan Assembly Steps
Begin with a Microstation seed file
Attach coordinate correct reference files (roadway mapping and alignments)

## Slide 4: Signing Plan Assembly Steps
Place all signs on roadway plan sheet for each direction of travel (Use figures in TEM and MN MUTCD)

## Slide 5: Signing Plan Assembly Steps
Place all signs on roadway plan sheet for each direction of travel (Use figures in TEM and MN MUTCD)
  See MN MUTCD and TEM for placement and spacing
  Design all necessary guide signs in SignCAD
    Refer to MnDOT Traffic Guide Sign Design Manual for standards and procedures

## Slide 6: Signing Plan Assembly Steps
Label signs in an orderly fashion beginning at the left edge of the first sheet and progressing through the last roadway sheet
  NOTE: refer to the TEM Chapter 6 section 6-4 for information on how MnDOT classifies signs by design type (A, C, D, EA, EO and OH)
  New signs get labeled with their sign type and a unique A type number similar to an OH sign number.
    EXAMPLE: A I94-001, A I94-002, A MN280-001 etc. for new A signs. C-1, C-2, C-3 etc. for new C signs. D-1, D-2, for new D signs

## Slide 7: Signing Plan Assembly Steps
  Existing signs being removed are labeled with their sign type and a sequential number beginning with 101
  Except Type C signs and Delineators and Markers
    EXAMPLE: A I94-101, A I04-102, A MN280-101 etc. for Type A signs being removed. D-101, D-102, for Type D signs being removed. * C signs being removed DO NOT NEED TO BE LABELLED THIS WAY. C signs are shown on the roadway and totaled in the Statement of Estimated quantities, but do not need to be labelled C-101, C102) *See sample Signing plans.
  Existing signs being Salvaged are labelled with their sign type and a sequential number beginning with 201
    EXAMPLE: A I94-201, A I94-202. C-201, C-202 etc.
  All completely identical Type C, D, EA, and EO signs receive the same label throughout the plan.

## Slide 8: Signing Plan Assembly Steps
  Circled numbers (notes) describing the work to be done to the sign follow the label
  Notes 1 through 6 describe common signing situations or tasks and are consistent in all signing plans

## Slide 9: Signing Plan Assembly Steps
  Notes 7 and beyond will vary by plan depending on the work required in the individual signing plan
  Type OH signs have a unique numbers assigned to them. Contact the OTST Signing Unit to obtain new OH sign numbers (Brian Barrett 651-234-7374)

## Slide 10: Signing Plan Assembly Steps

## Slide 11: Signing Plan Assembly Steps
Show appropriate delineation and markers
  See TEM Chapter 6 for details
  A note may be used to indicate standard delineation at standard exit ramp/loops
  See sample Signing plans.

## Slide 12: Signing Plan Assembly Steps
Organize roadway into plan sheets
  Begin with mainline roadway from start to finish of the project.
  Stationing generally increasing from left to right
  Interchange/intersections follow mainline roadway
  Label all roadways, cross streets and bridges
  Place “north” arrow and scale on all sheets
  Eliminate all unnecessary elements in the file
  When all the sign panels, delineators and markers are placed on the roadway layouts, with labels and notes, and the roadway layouts are organized into plan sheets, the plan is considered 60% complete. It is ready for initial review. Print outs of these roadway layouts, and Type A, D, EA, EO and OH panel designs should be submitted to MnDOT for review.

## Slide 13: Signing Plan Assembly Steps
Utilities: Compile a list of the utility companies within the project limits for inclusion in the plan
NOTE: Follow Utility Manual processes

## Slide 14: Signing Plan Assembly Steps
Design Type A and OH sign structures following the cross section format in the sample plan (Freeways Class)
Create estimated quantities tabulation and appropriate data boxes for each sign type and the work being done to the sign
  Master Tabs and Sample Plan

## Slide 15: Signing Plan Assembly Steps
Assemble all necessary structural and detail sheets
Complete the title sheet (if signing plan is not part of a larger construction project)
Assemble all plan sheets in their proper order (see sample plan)
Number all plan sheets
Verify all cross sheet referencing in the plan

## Slide 16: Title Sheet
Plan Description & Location

## Slide 17: Title Sheet
Governing Specs &
Index of Sheets

## Slide 18: Title Sheet
Project Numbers

## Slide 19: Title Sheet
Plan Approvals/Certification

## Slide 20: Title Sheet
Index Map
Index Map

## Slide 21: Title Sheet
Begin/End Stations

## Slide 22: Sample Plan

## Slide 23: Title Sheet
Project Location
Plan & Map Scales

## Slide 24: Title Sheet
Plan Revisions Table

## Slide 25: Estimated Quantities
For list of items, see Spec Book
List of Pay Items

## Slide 26: Estimated Quantities

## Slide 27: Type C Sign Data Sheet Chart A and Chart B
Chart A for signs to be furnished and installed
Chart B for signs to be salvaged and installed

## Slide 28: Type C Sign Data Sheet Chart A
Order in accordance with the Standard Signs Summary
Regulatory
Warning
Route Markers & Auxiliaries
Sign Number

## Slide 29: Type C Sign Data Sheet Chart A
Order
Quantity

## Slide 30: Type C Sign Data Sheet Chart A
Number of Posts, Type, and Knee Brace Quantity
TEM Charts 6.2
Length
Post Length Determination Sheet
Posts

## Slide 31: Type C Sign Data Sheet Chart A
Mounting Height

## Slide 32: Type C Sign Data Sheet Chart A
Panel Summary
Size specified in the Standard Signs Summary
STOP signs specified in TEM 6-5.12

## Slide 33: Type C Sign Data Sheet Chart A
Code Number, Panel Legend
Code specified in the Standard Signs Summary

## Slide 34: Type C Sign Data Sheet Chart A
Specific Notes

## Slide 35: Type C Sign Data Sheet Chart A
General Notes

## Slide 36: Type C Sign Data Sheet Chart B
Same information as Chart A, however,
Chart B is for Signs to be salvaged and installed

## Slide 39: Type C Sign Data Sheet Charts C
Post Spacing
  Punch Codes in Standard Signs Manual or
  TEM Chart 6.4
Panel Legend (graphic)
  Details on later sheet

## Slide 41: Type D Sign Data Sheet Chart D and E

## Slide 42: Chart E

## Slide 43: Chart F, G and H

## Slide 44: Chart F

## Slide 45: Type D Sign Data Sheet Chart G - Markers

## Slide 47: Utilities
Follow the Utility Manual Processes

## Slide 48: Utilities
Affect on Utilities

## Slide 49: Utilities
Subsurface Utility Info

## Slide 50: Utilities
List of Utilities

## Slide 51: Roadway Layout
Stationing

## Slide 52: Roadway Layout
Sign Numbers

## Slide 53: Roadway Layout
Sign Locations

## Slide 54: Roadway Layout
Notes

## Slide 55: Type D Sign Panels
  SignCAD software used to design panels
  Sign panel dimensioning
  See Standard Signs and Pavement Markings Manual for arrow, fraction and overlay details.
  Guide Sign Design Course offered in July

## Slide 56: Sign Placement
TEM Figure 6.1

## Slide 57: Delineators & Markers

## Slide 58: Type C & D Signs Structural Details
TEM Charts 6.3 and 6.4

## Slide 59: Type C & D Signs Structural Details

## Slide 60: Type C Signs, Delineators & Markers in Concrete

## Slide 61: Type C and D Structural Steel Mounting System for Round Supports

## Slide 62: Common Plan Set Issues
The following is a list of some of the common issues with plan sets from MnDOT reviewers
These are not in any order of importance

## Slide 63: Common TTC Plan Set Issues

## Slide 64: Common TTC Plan Set Issues

## Slide 65: Design Scene
A guidance document for designers, technicians and engineers to help improve the quality and reduce cost and time of plan preparation